## Slide 1: PAW-VENTX Residential Counterflow Ventilation

## Slide 2: NEW PAW-VENTX Residential Counterflow Ventilation units
PAW-VENTX... |  |  | 
 | 20/30/40 V | 20/30/40 H | 10/15 Z
Install type: | Vertical | Horizonal | Vertical / Horizontal
Airflow range | 112 – 375 m3 | 112 – 375 m3 | 72 – 133 m3
Widened application range now supported
Complements our existing residential solutions line-up
Suitable for a variety of installation requirements
Price-competitive solution

## Slide 3: Topics for today’s webinar
Why ventilation is important:
Political drivers (EU direction, EPBD)
Energetic aspects
Health and comfort (disease prevention, air quality etc.)
Building Protection
How to ventilate:
Ventilation theory
System types (natural, mechanical and heat recovery)
NEW VENTX HRV units

## Slide 4: Why Ventilation
“In the European Union, buildings alone account for as much as 40% of total energy consumption. And are also responsible for 36% of direct/indirect greenhouse gas emissions related to energy consumption.” (1)
With these conditions it is necessary to reduce building emissions to combat climate change and the greenhouse effect
1. Source: European Council

## Slide 5: Why Ventilation
European Performance of Buildings Directive (EPBD)
To boost energy performance of buildings, the EU has established a legislative framework that includes the Energy Performance of Buildings Directive 2010/31/EU and the Energy Efficiency Directive 2012/27/EU.
Both directives were amended in 2018 and 2019, as part of the “Clean Energy package”
In 2020, proposal to revise the EPBD to support the Renovation Wave Strategy – which aims to double the energy renovation rate by 2030
1. Source: European Council
“The EPBD is a constantly evolving instrument and aims - in time - to phase out buildings with inadequate energy performance.”
Improved quality of life
Health benefits
Alleviate energy poverty
Create ‘green’ jobs

## Slide 6: Why Ventilation
Chart: Building Energy Losses
| Roof | Floor | Walls | Windows & doors | Ventilation
Column1 | 6 | 9 | 22 | 32 | 31
In a residential property, the energy lost through ventilation accounts for one of the greatest factors
Source: Open University

## Slide 7: Why Ventilation
Increased standards for insulation have also led to
ventilation decreasing, resulting in poorer indoor air quality (IAQ) levels.
A very well insulated house, means a very airtight house.
On average, we spend 90% of our time indoors.
This means the impact of poor IAQ is very high.

## Slide 8: Why Ventilation
Source: ASHRAE Trans. 91 – 1B (1985)
microorganism proliferation
ideal area for human health
Bacteria
Virus
Mould
Mites
Humidity (%)
Ventilation systems help to manage humidity levels by removing moist air from the building

## Slide 9: Why Ventilation
Desirable
1000 ppm
1200 ppm
Acceptable
Poor
1500 ppm
> 5000 ppm
Dangerous
CO2 levels should be controlled to maintain health and well-being

## Slide 10: Why Ventilation
Old Filtration class: EN 779
Rated air filters from G1-F9
NEW Filtration class: ISO 16890
Based on particulate matter groups

## Slide 11: Why Ventilation
ePM1 0.3 – 1.0 µm | ePM2.5 0.3 – 2.5 µm | eMP10 0.3 – 10 µm | Coarse
ePM1 95 % | ePM2.5 95 % | ePM10 95 % | Coarse 95 %
ePM1 90 % | ePM2.5 90 % | ePM10 90 % | ISO Coarse
ePM1 85 % | ePM2.5 85 % | ePM10 85 % | 
ePM1 80 % | ePM2.5 80 % | ePM10 80 % | 
ePM1 75 % | ePM2.5 75 % | ePM10 75 % | 
ePM1 70 % | ePM2.5 70 % | ePM10 70 % | 
↓ ePM1 50 % | ↓ ePM2.5 50 % | ↓ ePM10 50 % | ↓ Coarse 5%
Example B:
This filter collects:
72 % of the PM1 fraction
76 % of the PM2 fraction
90 % of the PM3 fraction
Therefore, it is assigned ePM1 70 %
Example A:
This filter collects:
42 % of the PM1 fraction
66 % of the PM2 fraction
70 % of the PM3 fraction
Therefore, it is assigned ePM2 65 %

## Slide 12: How to Ventilate
Residential Ventilation Systems
Natural Ventilation
Horizontal transverse ventilation
Shaft ventilation
Mechanical Ventilation
Extract ventilation
Supply and extract ventilation
Hybrid Ventilation
Natural + extract ventilation
Natural + S/E ventilation
Image Source: Energy Saving Trust

## Slide 13: How to Ventilate
Image Source: Energy Saving Trust

## Slide 14: How to Ventilate
Heat recovery not possible
Unstable air temperatures
Free cooling
No running cost
Airflow is not controlled
Natural Ventilation
Sensible / enthalpic heat recovery
Thermal comfort
Free cooling with summer bypass
Fan power consumption
Controlled airflow
Mechnical Ventilation

## Slide 15: How to ventilate
A recuperative heat exchanger is an enclosure with a series if plates (ribs), which allow extracted air to pass over incoming fresh air. The heated fresh air can then be used as supply air for the building
Supply
Extract
Fresh
Exhaust
Supply
Exhaust
Fresh
Extract

## Slide 16: How to Ventilate
Counter-flow
heat exchanger
Supply
Extract
Fresh
Exhaust
Cross-flow
heat exchanger
Extract
Supply
Fresh
Exhaust
Cross counter-flow
heat exchanger
Extract
Supply
Exhaust
Fresh

## Slide 17: How to Ventilate
Supply
19 °C
Fresh
-12 °C
Exhaust
-2 °C
Fresh
-12 °C
Extract
22 °C
Extract
22 °C
Exhaust
-9 °C
Supply
12 °C
Cross-flow
heat exchanger
Cross counter-flow
heat exchanger

## Slide 18: NEW PAW-VENTX Range
Horizontal mounting unit (H)
Horizontal mounting (possible for some false ceilings)
Suitable for single family houses, with nominal air flow rates up to 350 m³/h
Easily accessible lower panel for maintenance and inspection
Vertical mounting unit (V)
Vertical mounting (typically in a technical room)
Suitable for single family houses, with nominal air flow rates up to 350 m³/h
Easily accessible front panel for maintenance and inspection
Universal mounting compact unit (Z)
Universal mounting (horizontal or vertical)
Suitable for small and medium size apartments, with nominal air flow up to 200 m³/h

## Slide 19: NEW PAW-VENTX Range
Airflow Range
91 m3/h
380 m3/h
PAW-VENTX... |  |  | 
 | 20/30/40 V | 20/30/40 H | 10/15 Z
Install type: | Vertical | Horizonal | Vertical / Horizontal
Airflow range | 112 – 375 m3 | 112 – 375 m3 | 72 – 133 m3
292 m3/h

## Slide 20: NEW PAW-VENTX Range
Structure: self-supporting sheet metal frame, interior in high density EPS 30 kg/m³ and polyethylene foam. Carpentry and internal plugging in thick galvanised sheet metal.
Heat exchanger: counter-current type. Sensible version in polypropylene, enthalpic version with breathable membranes(1).
Brushless fans: DC fans regulated by inverters allow high levels of comfort and energy efficiency with constant flow function.
Filters: EPM1 filter on fresh air and extract air with low pressure drop. Easily removable for routine maintenance.
1. Not available at present.

## Slide 21: NEW PAW-VENTX Range
A: Pre-heating required below -7 °C
Summer operation limit
Outoor temperature (°C)
Indoor
temperature
(°C)
PAW-VEN-HTR05: Electrical duct heater 0.5 kW
PAW-VEN-HTR10: Electrical duct heater 1.0 kW
Winter operation limit
Indoor
temperature
(°C)
Outoor temperature (°C)
A

## Slide 22: NEW PAW-VENTX Range
Remote control available in black and white options:
PAW-VEN-CNTRLB
PAW-VEN-CNTRLW
Both contain built-in VOC and humidity sensors as standard

## Slide 23: NEW PAW-VENTX Range
Heat Recovery Ventilation
Control of IAQ
Filtering outdoor air
Control of internal equilibrium pressure
All seasons
Anti-freezing protocol
Control of internal humidity, increase ventilation ratio
Winter
Free cooling or summer bypass
Control of internal humidity, decrease ventilation ratio
Summer

## Slide 24: NEW PAW-VENTX Range
Makes ventilation speed adjustment fully automatically according to IAQ values is RH %
Allows you to set the minimum ventilation speed
Allows you to set the rated ventilation speed / Allows you to set the desired humidity value
Allows you to set the maximum ventilation speed
Static pressure
Air volume
PAW-VENTX40H Fan Performance Curve

## Slide 25: NEW PAW-VENTX Range
Each unit can be configured in one of two ways (A/B), depending on the installation
A: Factory configuration | B: Modification on-site

## Slide 26: NEW PAW-VENTX Range
If configuration B is chosen, alternate drain connections, sensor terminals and label must be used

## Slide 27: PAW-VENTX Range
Specific Power Input:
Specific Power Input (SPI) is a parameter that quantifies system energy efficiency. A measure of electric power required relative to the amount of air moved [kW/(m³/h)].
Specific Fan Power:
Specific Fan Power (SFP) is a parameter that quantifies fan energy efficiency. A measure of electric power required relative to the amount of air moved [kW/(m³/s)].

## Slide 28: PAW-VENTX Range
All units will have a be in Energy Class A
We comply with Danish Regulation DK BR18
 |  |  |  |  | CLASS A | SPI < 0.28
 | Max. m3/h | Pa | Ref. m3/h | Pa | SEC Class | SPI W/m3/h
VENTX10Z | 130 | 100 | 91 | 50 | A | 0.242
VENTX15Z | 210 | 100 | 147 | 50 | A | 0.313
VENTX20H | 155 | 100 | 109 | 50 | A | 0.276
VENTX20V | 170 | 100 | 112 | 50 | A | 0.277
VENTX30H | 300 | 100 | 210 | 50 | A | 0.271
VENTX30V | 300 | 100 | 210 | 50 | A | 0.276
VENTX40H | 340 | 100 | 238 | 50 | A | 0.265
VENTX40V | 380 | 100 | 266 | 50 | A | 0.256

## Slide 29
PAW-VENTX Residential Counterflow Ventilation
Price competitive product range which delivers great value
In-line with the global direction of building development and climate control strategies
Compliments available range of Panasonic solutions
Suitable for a wide range of applications; highly versatile range which is installation friendly

## Slide 31: NEW PAW-VENTX Range
PAW- |  | VENTX10Z | VENTX15Z | VENTX20H | VENTX20V | VENTX30H | VENTX30V | VENTX40H | VENTX40V
Air flow (Nom/Max) | M3/h | 91 / 130 | 147 / 210 | 109 / 155 | 112 / 170 | 210 / 300 | 210 / 300 | 238 / 340 | 266 / 380
Static pressure (nom/max) | Pa | 50 / 100 | 50 / 100 | 50 / 100 | 50 / 100 | 50 / 100 | 50 / 100 | 50 / 100 | 50 / 100
Type of HEX |  | Counter flow HRV / Sensible |  |  |  |  |  |  | 
Recovery Efficiency | % | 87 | 85 | 86 | 86 | 85 | 86 | 89 | 87
Energy class |  | A | A | A | A | A | A | A | A
Power supply | V/Hz | 230 / 50 | 230 / 50 | 230 / 50 | 230 / 50 | 230 / 50 | 230 / 50 | 230 / 50 | 230 / 50
Power consumption (nom) | W | 80 | 140 | 110 | 110 | 180 | 180 | 350 | 350
Sound power LWA | Db(A) | 48 | 51 | 49 | 48 | 50 | 50 | 52 | 51

## Slide 32: NEW PAW-VENTX Range
Model Code |  | VENTX10Z | VENTX15Z | VENTX20H | VENTX20V | VENTX30H | VENTX30V | VENTX40H | VENTX40V
Dimensions | mm | 580 x 580 x 255 | 580 x 580 x 255 | 800 x 480 x 260 | 625 x 430 x 510 | 795 x 600 x 295 | 785 x 575 x 590 | 1150 x 650 x 290 | 785 x 735 x 590
Weight | kg | 19 | 19 | 25 | 32 | 300 | 38 | 38 | 42
Mounting position |  | Hor / Ver | Hor / Ver | Horizontal | Vertical | Horizontal | Vertical | Horizontal | Vertical
Filter class |  | ePMI 80% | ePMI 80% | ePMI 80% | ePMI 80% | ePMI 70% | ePMI 70% | ePMI 70% | ePMI 70%
Duct connections | mm | 160 | 160 | 160 | 160 | 160 | 160 | 160 | 160